## Slide 1: Instruction Set Architecture
Assembly Language View
  Processor state
    Registers, memory, …
  Instructions
    addl, pushl, ret, …
    How instructions are encoded as bytes
Layer of Abstraction
  Above: how to program machine
    Processor executes instructions in a sequence
  Below: what needs to be built
    Use variety of tricks to make it run fast
    E.g., execute multiple instructions simultaneously
ISA
Compiler
OS
CPU
Design
Circuit
Design
Chip
Layout
Application
Program

## Slide 2: CISC Instruction Sets
  Complex Instruction Set Computer
  Dominant style through mid-80’s
Stack-oriented instruction set
  Use stack to pass arguments, save program counter
  Explicit push and pop instructions
Arithmetic instructions can access memory
  addl %eax, 12(%ebx,%ecx,4)
    requires memory read and write
    Complex address calculation
Condition codes
  Set as side effect of arithmetic and logical instructions
Philosophy
  Add instructions to perform “typical” programming tasks

## Slide 3: RISC Instruction Sets
  Reduced Instruction Set Computer
  Internal project at IBM, later popularized by Hennessy (Stanford) and Patterson (Berkeley)
Fewer, simpler instructions
  Might take more to get given task done
  Can execute them with small and fast hardware
Register-oriented instruction set
  Many more (typically 32) registers
  Use for arguments, return pointer, temporaries
Only load and store instructions can access memory
  Similar to Y86 mrmovl and rmmovl
No Condition codes
  Test instructions return 0/1 in register

## Slide 4: MIPS Registers

## Slide 5: MIPS Instruction Examples
Op
Ra
Rb
Offset
Op
Ra
Rb
Rd
Fn
00000
R-R
Op
Ra
Rb
Immediate
R-I
Load/Store
addu $3,$2,$1 # Register add: $3 = $2+$1
addu $3,$2, 3145 # Immediate add: $3 = $2+3145
sll $3,$2,2 # Shift left: $3 = $2 << 2
lw $3,16($2) # Load Word: $3 = M[$2+16]
sw $3,16($2) # Store Word: M[$2+16] = $3
Op
Ra
Rb
Offset
Branch
beq $3,$2,dest # Branch when $3 = $2

## Slide 6: CISC vs. RISC
Original Debate
  Strong opinions!
  CISC proponents---easy for compiler, fewer code bytes
  RISC proponents---better for optimizing compilers, can make run fast with simple chip design
Current Status
  For desktop processors, choice of ISA not a technical issue
    With enough hardware, can make anything run fast
    Code compatibility more important
  For embedded processors, RISC makes sense
    Smaller, cheaper, less power
    Most cell phones use ARM processor

## Slide 7: Y86 Processor State
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
ZF
SF
OF
  Program Registers
    Same 8 as with IA32. Each 32 bits
  Condition Codes
    Single-bit flags set by arithmetic or logical instructions
      ZF: Zero SF:Negative OF: Overflow
  Program Counter
    Indicates address of next instruction
  Program Status
    Indicates either normal operation or some error condition
  Memory
    Byte-addressable storage array
    Words stored in little-endian byte order
RF: Program registers
CC: Condition codes
PC
DMEM: Memory
Stat: Program status

## Slide 8: Y86 Instructions
Format
  1–6 bytes of information read from memory
    Can determine instruction length from first byte
    Not as many instruction types, and simpler encoding than with IA32
  Each accesses and modifies some part(s) of the program state

## Slide 9: Encoding Registers
Each register has 4-bit ID
  Same encoding as in IA32
Register ID 15 (0xF) indicates “no register”
  Will use this in our hardware design in multiple places
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
0
1
2
3
6
7
4
5

## Slide 10: Instruction Example
Addition Instruction
  Add value in register rA to that in register rB
    Store result in register rB
    Note that Y86 only allows addition to be applied to register data
  Set condition codes based on result
  e.g., addl %eax,%esi Encoding: 60 06
  Two-byte encoding
    First indicates instruction type
    Second gives source and destination registers
addl rA, rB
6
0
rA
rB
Encoded Representation
Generic Form

## Slide 11: Arithmetic and Logical Operations
  Encodings differ only by “function code”
  Set condition codes as side effect
addl rA, rB
6
0
rA
rB
subl rA, rB
6
1
rA
rB
andl rA, rB
6
2
rA
rB
xorl rA, rB
6
3
rA
rB
Add
Subtract (rA from rB)
And
Exclusive-Or
Instruction Code
Function Code

## Slide 12: Move Operations
  Like the IA32 movl instruction
  Simpler format for memory addresses
  Give different names to keep them distinct
rrmovl rA, rB
2
0
rA
rB
Register --> Register
Immediate --> Register
irmovl V, rB
3
0
F
rB
V
Register --> Memory
rmmovl rA, D(rB)
4
0
rA
rB
D
Memory --> Register
mrmovl D(rB), rA
5
0
rA
rB
D

## Slide 13: Move Instruction Examples
irmovl $0xabcd, %edx
movl $0xabcd, %edx
30 f2 cd ab 00 00
IA32
Y86
Encoding
rrmovl %esp, %ebx
movl %esp, %ebx
20 43
mrmovl -12(%ebp),%ecx
movl -12(%ebp),%ecx
50 15 f4 ff ff ff
rmmovl %esi,0x41c(%esp)
movl %esi,0x41c(%esp)
—
movl $0xabcd, (%eax)
—
movl %eax, 12(%eax,%edx)
—
movl (%ebp,%eax,4),%ecx
40 64 1c 04 00 00

## Slide 14: Conditional Move Instructions
  Refer to generically as “cmovXX”
  Encodings differ only by “function code”
  Based on values of condition codes
  Variants of rrmovl instruction
    (Conditionally) copy value from source to destination register
rrmovl rA, rB
Move Unconditionally
cmovle rA, rB
Move When Less or Equal
cmovl rA, rB
Move When Less
cmove rA, rB
Move When Equal
cmovne rA, rB
Move When Not Equal
cmovge rA, rB
Move When Greater or Equal
cmovg rA, rB
Move When Greater
2
0
rA
rB
2
1
rA
rB
2
2
rA
rB
2
3
rA
rB
2
4
rA
rB
2
5
rA
rB
2
6
rA
rB

## Slide 15: Jump Instructions
  Refer to generically as “jXX”
  Encodings differ only by “function code”
  Based on values of condition codes
  Same as IA32 counterparts
  Encode full destination address
    Unlike PC-relative addressing seen in IA32
jmp Dest
7
0
Jump Unconditionally
Dest
jle Dest
7
1
Jump When Less or Equal
Dest
jl Dest
7
2
Jump When Less
Dest
je Dest
7
3
Jump When Equal
Dest
jne Dest
7
4
Jump When Not Equal
Dest
jge Dest
7
5
Jump When Greater or Equal
Dest
jg Dest
7
6
Jump When Greater
Dest

## Slide 16: Y86 Program Stack
  Region of memory holding program data
  Used in Y86 (and IA32) for supporting procedure calls
  Stack top indicated by %esp
    Address of top stack element
  Stack grows toward lower addresses
    Top element is at lowest address in the stack
    When pushing, must first decrement stack pointer
    After popping, increment stack pointer
%esp
•
•
•
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 17: Stack Operations
  Decrement %esp by 4
  Store word from rA to memory at %esp
  Like IA32
  Read word from memory at %esp
  Save in rA
  Increment %esp by 4
  Like IA32
pushl rA
A
0
rA
F
popl rA
B
0
rA
F

## Slide 18: Subroutine Call and Return
  Push address of next instruction onto stack
  Start executing instructions at Dest
  Like IA32
  Pop value from stack
  Use as address for next instruction
  Like IA32
call Dest
8
0
Dest
ret
9
0

## Slide 19: Miscellaneous Instructions
  Don’t do anything
  Stop executing instructions
  IA32 has comparable instruction, but can’t execute it in user mode
  We will use it to stop the simulator
  Encoding ensures that program hitting memory initialized to zero will halt
nop
1
0
halt
0
0

## Slide 20: Y86 Instruction Set #1
Byte
0
1
2
3
4
5
pushl rA
A
0
rA
F
jXX Dest
7
fn
Dest
popl rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovl V, rB
3
0
F
rB
V
rmmovl rA, D(rB)
4
0
rA
rB
D
mrmovl D(rB), rA
5
0
rA
rB
D
OPl rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0

## Slide 21: Y86 Instruction Set #2
Byte
0
1
2
3
4
5
pushl rA
A
0
rA
F
jXX Dest
7
fn
Dest
popl rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovl V, rB
3
0
F
rB
V
rmmovl rA, D(rB)
4
0
rA
rB
D
mrmovl D(rB), rA
5
0
rA
rB
D
OPl rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
rrmovl
2
0
cmovle
2
1
cmovl
2
2
cmove
2
3
cmovne
2
4
cmovge
2
5
cmovg
2
6

## Slide 22: Y86 Instruction Set #3
Byte
0
1
2
3
4
5
pushl rA
A
0
rA
F
jXX Dest
7
fn
Dest
popl rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovl V, rB
3
0
F
rB
V
rmmovl rA, D(rB)
4
0
rA
rB
D
mrmovl D(rB), rA
5
0
rA
rB
D
OPl rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
addl
6
0
subl
6
1
andl
6
2
xorl
6
3

## Slide 23: Y86 Instruction Set #4
Byte
0
1
2
3
4
5
pushl rA
A
0
rA
F
jXX Dest
7
fn
Dest
popl rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovl V, rB
3
0
F
rB
V
rmmovl rA, D(rB)
4
0
rA
rB
D
mrmovl D(rB), rA
5
0
rA
rB
D
OPl rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6

## Slide 24: Status Conditions
Mnemonic | Code
ADR | 3
Mnemonic | Code
INS | 4
Mnemonic | Code
HLT | 2
Mnemonic | Code
AOK | 1
  Normal operation
  Halt instruction encountered
  Bad address (either instruction or data) encountered
  Invalid instruction encountered
Desired Behavior
  If AOK, keep going
  Otherwise, stop program execution

## Slide 25: Y86 Sample Program Structure #1
  Program starts at address 0
  Must set up stack
    Where located
    Pointer values
    Make sure don’t overwrite code!
  Must initialize data
init: # Initialization
. . .
call Main
halt
.align 4 # Program data
array:
. . .
Main: # Main function
. . .
call len2
. . .
len2: # Length function
. . .
.pos 0x100 # Placement of stack
Stack:

## Slide 26: Y86 Program Structure #2
  Program starts at address 0
  Must set up stack
  Must initialize data
  Can use symbolic names
init:
irmovl Stack, %esp # Set up SP
irmovl Stack, %ebp # Set up FP
call Main # Execute main
halt # Terminate
# Array of 4 elements + terminating 0
.align 4
array:
.long 0x000d
.long 0x00c0
.long 0x0b00
.long 0xa000
.long 0

## Slide 27: Y86 Program Structure #3
Set up call to len2
  Follow IA32 procedure conventions
  Push array address as argument
Main:
pushl %ebp
rrmovl %esp,%ebp
irmovl array,%edx
pushl %edx # Push array
call len2 # Call len2(array)
pop %edx
popl %ebp
ret

## Slide 28: Assembling Y86 Program
  Generates “object code” file len.yo
    Actually looks like disassembler output
  unix> yas len.ys
  0x000: | .pos 0
  0x000: 30f400010000 | init: irmovl Stack, %esp # Set up stack pointer
  0x006: 30f500010000 | irmovl Stack, %ebp # Set up base pointer
  0x00c: 8028000000 | call Main # Execute main program
  0x011: 00 | halt # Terminate program
  |
  | # Array of 4 elements + terminating 0
  0x014: | .align 4
  0x014: | array:
  0x014: 0d000000 | .long 0x000d
  0x018: c0000000 | .long 0x00c0
  0x01c: 000b0000 | .long 0x0b00
  0x020: 00a00000 | .long 0xa000
  0x024: 00000000 | .long 0

## Slide 29: Simulating Y86 Program
  Instruction set simulator
    Computes effect of each instruction on processor state
    Prints changes in state from original
  unix> yis len.yo
  Stopped in 50 steps at PC = 0x11. Status 'HLT', CC Z=1 S=0 O=0
  Changes to registers:
  %eax: 0x00000000 0x00000004
  %ecx: 0x00000000 0x00000004
  %edx: 0x00000000 0x00000028
  %esp: 0x00000000 0x00000100
  %ebp: 0x00000000 0x00000100
  Changes to memory:
  0x00ec: 0x00000000 0x000000f8
  0x00f0: 0x00000000 0x00000039
  0x00f4: 0x00000000 0x00000014
  0x00f8: 0x00000000 0x00000100
  0x00fc: 0x00000000 0x00000011

## Slide 30: Overview of Logic Design
Fundamental Hardware Requirements
  Communication
    How to get values from one place to another
  Computation
  Storage
Bits are Our Friends
  Everything expressed in terms of values 0 and 1
  Communication
    Low or high voltage on wire
  Computation
    Compute Boolean functions
  Storage
    Store bits of information

## Slide 31: Digital Signals
  Use voltage thresholds to extract discrete values from continuous signal
  Simplest version: 1-bit signal
    Either high range (1) or low range (0)
    With guard range between them
  Not strongly affected by noise or low quality circuit elements
    Can make circuits simple, small, and fast
Voltage
Time
0
1
0

## Slide 32: Computing with Logic Gates
  Outputs are Boolean functions of inputs
  Respond continuously to changes in inputs
    With some, small delay
Voltage
Time
a
b
a && b
Rising Delay
Falling Delay

## Slide 33: Combinational Circuits
Acyclic Network of Logic Gates
  Continously responds to changes on primary inputs
  Primary outputs become (after some delay) Boolean functions of primary inputs
Acyclic Network
Primary
Inputs
Primary
Outputs

## Slide 34: Bit Equality
  Generate 1 if a and b are equal
Hardware Control Language (HCL)
  Very simple hardware description language
    Boolean operations have syntax similar to C logical operations
  We’ll use it to describe control logic for processors
Bit equal
a
b
eq
bool eq = (a&&b)||(!a&&!b)
HCL Expression

## Slide 35: Word Equality
  32-bit word size
  HCL representation
    Equality operation
    Generates Boolean value
b31
Bit equal
a31
eq31
b30
Bit equal
a30
eq30
b1
Bit equal
a1
eq1
b0
Bit equal
a0
eq0
Eq
=
B
A
Eq
Word-Level Representation
bool Eq = (A == B)
HCL Representation

## Slide 36: Bit-Level Multiplexor
  Control signal s
  Data signals a and b
  Output a when s=1, b when s=0
Bit MUX
b
s
a
out
bool out = (s&&a)||(!s&&b)
HCL Expression

## Slide 37: Word Multiplexor
  Select input word A or B depending on control signal s
  HCL representation
    Case expression
    Series of test : value pairs
    Output value for first successful test
Word-Level Representation
HCL Representation
b31
s
a31
out31
b30
a30
out30
b0
a0
out0
int Out = [
0 : A;
1 : B;
];
s
B
A
Out
MUX

## Slide 38: Arithmetic Logic Unit
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
  Combinational logic
    Continuously responding to inputs
  Control signal selects function computed
    Corresponding to 4 arithmetic/logical operations in Y86
  Also computes values for condition codes
A
L
U
Y
X
X + Y
0
A
L
U
Y
X
X - Y
1
A
L
U
Y
X
X & Y
2
A
L
U
Y
X
X ^ Y
3
A
B
A
B
A
B
A
B

## Slide 39: Storing and Accessing 1 Bit
Q+
Q–
R
S
R-S Latch
Resetting
1
0
1
0
0
1
Setting
0
1
0
1
1
0
Storing
0
0
!q
q
q
!q
Bistable Element
Q+
Q–
q
!q
q = 0 or 1

## Slide 40: Registers
  Stores word of data
    Different from program registers seen in assembly code
  Collection of edge-triggered latches
  Loads input on rising edge of clock
I
O
Clock
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
i7
i6
i5
i4
i3
i2
i1
i0
o7
o6
o5
o4
o3
o2
o1
o0
Clock
Structure

## Slide 41: Register File
  Stores multiple words of memory
    Address input specifies which word to read or write
  Register file
    Holds values of program registers
    %eax, %esp, etc.
    Register identifier serves as address
      ID 15 (0xF) implies no read or write performed
  Multiple Ports
    Can read and/or write multiple words in one cycle
      Each has separate address and data input/output
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Read ports
Write port
Clock

## Slide 42: Building Blocks
Combinational Logic
  Compute Boolean functions of inputs
  Continuously respond to input changes
  Operate on data and implement control
Storage Elements
  Store bits
  Addressable memories
  Non-addressable registers
  Loaded only as clock rises
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Clock
A
L
U
fun
A
B
MUX
0
1
=
Clock

## Slide 43: SEQ Hardware Structure
State
  Program counter register (PC)
  Condition code register (CC)
  Register File
  Memories
    Access same memory space
    Data: for reading/writing program data
    Instruction: for reading instructions
Instruction Flow
  Read instruction at address specified by PC
  Process through stages
  Update program counter
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 44: SEQ Stages
Fetch
  Read instruction from instruction memory
Decode
  Read program registers
Execute
  Compute value or address
Memory
  Read or write data
Write Back
  Write program registers
PC
  Update program counter
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 45: Instruction Decoding
Instruction Format
  Instruction byte icode:ifun
  Optional register byte rA:rB
  Optional constant word valC
5
0
rA
rB
D
icode
ifun
rA
rB
valC
Optional
Optional

## Slide 46: Computed Values
Fetch
  icode Instruction code
  ifun Instruction function
  rA Instr. Register A
  rB Instr. Register B
  valC Instruction constant
  valP Incremented PC
Decode
  srcA Register ID A
  srcB Register ID B
  dstE Destination Register E
  dstM Destination Register M
  valA Register value A
  valB Register value B
Execute
  valE ALU result
  Cnd Branch/move flag
Memory
  valM Value from memory

## Slide 47: SEQ Hardware
Key
  Blue boxes: predesigned hardware blocks
    E.g., memories, ALU
  Gray boxes: control logic
    Describe in HCL
  White ovals: labels for signals
  Thick lines: 32-bit word values
  Thin lines: 4-8 bit values
  Dotted lines: 1-bit values

## Slide 48: Fetch Logic
Predefined Blocks
  PC: Register containing PC
  Instruction memory: Read 6 bytes (PC to PC+5)
  Split: Divide instruction byte into icode and ifun
  Align: Get fields for rA, rB, and valC
Instruction
memory
PC
increment
rB
icode
ifun
rA
PC
valC
valP
Need
regids
Need
valC
Instr
valid
Align
Split
Bytes 1-5
Byte 0
imem_error
icode
ifun

## Slide 49: Fetch Logic
Control Logic
  Instr. Valid: Is this instruction valid?
  Need regids: Does this instruction have a register byte?
  Need valC: Does this instruction have a constant word?
Instruction
memory
PC
increment
rB
icode
ifun
rA
PC
valC
valP
Need
regids
Need
valC
Instr
valid
Align
Split
Bytes 1-5
Byte 0
imem_error
icode
ifun

## Slide 50: Decode Logic
Register File
  Read ports A, B
  Addresses are register IDs or 15 (0xF) (no access)
Control Logic
  srcA, srcB: read port addresses
rB
dstE
dstM
srcA
srcB
Register
file
A
B
M
E
dstE
dstM
srcA
srcB
icode
rA
valB
valA
valE
valM
Cnd

## Slide 51: Execute Logic
Units
  ALU
    Implements 4 required functions
    Generates condition code values
  CC
    Register with 3 condition code bits
  cond
    Computes conditional jump/move flag
Control Logic
  Set CC: Should condition code register be loaded?
  ALU A: Input A to ALU
  ALU B: Input B to ALU
  ALU fun: What function should ALU compute?
CC
ALU
ALU
A
ALU
B
ALU
fun.
Cnd
icode
ifun
valC
valB
valA
valE
Set
CC
cond

## Slide 52: Memory Logic
Memory
  Reads or writes memory word
Control Logic
  Mem. read: should word be read?
  Mem. write: should word be written?
  Mem. addr.: Select address
  Mem. data.: Select data
Data
memory
Mem.
read
Mem.
addr
read
write
data out
Mem.
data
valE
valM
valA
valP
Mem.
write
data in
icode
Stat
dmem_error
instr_valid
imem_error
stat

## Slide 53: Writeback
Register File
  Write ports E, M
  Addresses are register IDs or 15 (0xF) (no access)
Control Logic
  dstE, dstM: write port addresses
rB
dstE
dstM
srcA
srcB
Register
file
A
B
M
E
dstE
dstM
srcA
srcB
icode
rA
valB
valA
valE
valM
Cnd
Signals
  Cnd: Indicate whether or not to perform conditional move
    Computed in Execute stage

## Slide 54: PC Update Logic
New PC
  Select next value of PC
New
PC
Cnd
icode
valC
valP
valM
PC

## Slide 55: SEQ Hardware
Key
  Blue boxes: predesigned hardware blocks
    E.g., memories, ALU
  Gray boxes: control logic
    Describe in HCL
  White ovals: labels for signals
  Thick lines: 32-bit word values
  Thin lines: 4-8 bit values
  Dotted lines: 1-bit values

## Slide 56: Executing Arith./Logical Operation
Fetch
  Read 6 bytes
  Increment PC by 2
Decode
  Read operand registers
Execute
  Perform operation
  Set condition codes
Memory
  Do nothing
Write back
  Update register
PC Update
  Set PC to incremented PC value
OPl rA, rB
6
fn
rA
rB

## Slide 57: Executing rmmovl
Fetch
  Read 6 bytes
  Increment PC by 6
Decode
  Read operand registers
Execute
  Compute effective address
Memory
  Write to memory
Write back
  Do nothing
PC Update
  Set PC to incremented PC value
rmmovl rA, D(rB)
4
0
rA
rB
D

## Slide 58: Executing popl
Fetch
  Read 6 bytes
  Increment PC by 2
Decode
  Read stack pointer
Execute
  Increment stack pointer by 4
Memory
  Read from old stack pointer
Write back
  Update stack pointer
  Write result to register
PC Update
  Set PC to incremented PC value
popl rA
b
0
rA
F

## Slide 59: Executing Jumps
Fetch
  Read 6 bytes
  Increment PC by 5
Decode
  Do nothing
Execute
  Determine whether to take branch based on jump condition and condition codes
Memory
  Do nothing
Write back
  Do nothing
PC Update
  Set PC to Dest if branch taken or to incremented PC value if not branch
jXX Dest
7
fn
Dest
XX
XX
fall thru:
XX
XX
target:
Not taken
Taken

## Slide 60: Executing call
Fetch
  Read 6 bytes
  Increment PC by 5
Decode
  Read stack pointer
Execute
  Decrement stack pointer by 4
Memory
  Write incremented PC to new value of stack pointer
Write back
  Update stack pointer
PC Update
  Set PC to Dest
call Dest
8
0
Dest
XX
XX
return:
XX
XX
target:

## Slide 61: Executing ret
Fetch
  Read 6 byte
  Increment PC by 1
Decode
  Read stack pointer
Execute
  Increment stack pointer by 4
Memory
  Read return address from old stack pointer
Write back
  Update stack pointer
PC Update
  Set PC to return address
ret
9
0
XX
XX
return:

## Slide 62: SEQ Operation #1
State
  PC register
  Cond. Code register
  Data memory
  Register file
  All updated as clock rises
Combinational Logic
  ALU
  Control logic
  Memory reads
    Instruction memory
    Register file
    Data memory

## Slide 63: SEQ Operation #2
  state set according to second irmovl instruction
  combinational logic starting to react to state changes

## Slide 64: SEQ Operation #3
  state set according to second irmovl instruction
  combinational logic generates results for addl instruction

## Slide 65: SEQ Operation #4
  state set according to addl instruction
  combinational logic starting to react to state changes

## Slide 66: SEQ Operation #5
  state set according to addl instruction
  combinational logic generates results for je instruction